Technisonic TDFM-136 Radio

Power Up

- To power up the Technisonic TDFM radio make sure the Mission Master toggle switch is in the on position.  This switch is located just to the right of the co-pilots side control yoke.

- Desired Settings:

  - Main switch is turned on and set to a mid-volume level.

  - Guard volume switch is turned down.

  - MN/GD switch is set to MN.

  - HI/LO switch is in the LO position (use HI power only if needed, HI can distort or “motor-boat”)

- If you get in trouble with a command, press the */ESC key to escape the command.

- Use COM3 to listen and transmit on FM.

- Press TDFM Squelch to verify you are listening to COM3 and to set the “Main” Volume level.

Display Brightness

- To adjust the display brightness, use the 2 and 8 keys to increase/decrease the display brightness

Channel Selection

- The FM radio is pre-programmed with appropriate CAP frequencies.  See the communications section of the aircraft book for the channel plan.

- To scroll through channels use the 4 and 6 keys to scroll backwards and forwards through the channels.

- To select a channel by channel number, press the 1/CHAN key and enter a 3 digit channel (001 to 200) using the numeric key pad.  To accept the entry, press the #/ENTER key.  To abandon the selection, press the */ESC key.  Note the MN/GD switch MUST be in the MN position.

- Do not use the 7/FREQ key unless you know what you are doing.  If in doubt, use the */ESC key to get out of any command.

- If the keypad appears not to be responding, it may be locked.  To unlock the keypad, hold the */ESC key for two seconds.   This should unlock the keypad.

Talking on the radio

|  | The TDFM radio is COM3 on the audio panel. To monitor the FM radio, press “COM3” to illuminate it. Remember to do this on both audio panels for everyone to be listening to COM3 To transmit on the FM radio, press “COM3 MIC”. Note the selected MIC sets that COM to receive mode. The PTT switch will now transmit on the FM radio when pressed. |
| --- | --- |