Basic G1000 Mission Observer Quick Reference Guide

KEY:

B		Turn big (outer) knob

S    		Turn small (inner) knob

RANGE	Press named knob or softkey

ENT	   	Press named hardkey

All Tasks start at Map Page 1 (hold CLR for 2 seconds)

Mark and Save a Point

- Press RANGE once.

- Within 5 seconds press ENT

- B to “Create User Waypoint”

- ENT

- S left to ‘1’ (for first, ‘2’ for second…)

- ENT

- Hold CLR for 2 seconds ( Map Page 1

Retrieve & Delete Waypoint (post-flight)

- B to WPT page group.

- S to “User Waypoint” page.

- Press S knob to get cursor.

- B down to “User Waypoint List”, continue to “1”.

- Write down “Information” (Lat/Long info)

- DELETE softkey

- ENT to verify delete

- <repeat for all numbered waypoints>

Show Quarter Grid Lat/Longs

- Hold CLR for 2 seconds ( Map Page 1

- Turn RANGE knob until Map Scale shows “30nm”.

- If  lat/long lines are already showing, skip next Task “Enable Map Lat/Longs”.

Enable Map Lat/Longs

- MENU

- B to Map Setup

- ENT

- S to “Land”

- ENT

- B to “LAT/LON”

- Using B to move field to field, S to modify a field, and ENT to save:  Set ‘TEXT’ = Small, ‘RNG’ = 30nm

Mission Master – power on CAP-specific equipment (FM, DF)

FM Radio Setup

Main = Volume – set about halfway as shown Guard – turn all the way down (counter-clockwise) Squelch – press to verify you can hear the radio (COM3) White switches – up up down as shown Keypad: up / down arrows (2, 8) to set brightness left / right arrows (4, 6) to go up / down channels

Basic G1000 Mission Observer Quick Reference Guide

| Select Switches Setup |  |
| --- | --- |
| Good – both Green | Bad – either one blue |

| Comm Audio Panel Setup |  |
| --- | --- |
|  | Mic – select for transmitting Right side COM1, COM2, COM3 – all should be selected for listening Also select AUX to listen to Becker DF |

Becker Direction-Finding Setup

(1) Power on/off (or use Mission Master) During power-up, use Page Knob (2) to set Emergency or Training mode. You only have three seconds.

Use bottom right knob (1) to select Frequency Use Volume (2) to set Volume Use SQL (3) to set Squelch level (triangle in the black) Listen by selecting AUX on Comm audio panel If no signal is heard, try listening on COM2

Advanced G1000 MO Quick Reference Guide

Grid Search – Mission “Fast Launch” – set one corner

KEY:

B		Turn big (outer) knob

S    		Turn small (inner) knob

RANGE	Press named knob or softkey

ENT	   	Press named hardkey

All Tasks start at Map Page 1 (hold CLR for 2 seconds)

See next page for how-to modify all 4 grid points & create flight plan

Do this after Engine Start, before takeoff.  Eyes outside while plane is taxiing – do this only while plane is stationary

Clear all Flight Plans

- FPL

- S to “Flight Plan Catalog” page.

- MENU

- S  to “Delete All”

- ENT

- ENT

Modify 1 existing Waypoint:  GPTNW

- Go to Map Page 1 (hold CLR for 2 seconds)

- B to WPT page group.

- S to “User Waypoint” page.

- Press S knob to get cursor.

- B down to “User Waypoint List”, continue to GPTNW.

- ENT to get to detailed info & modify the waypoint

- B to “Information” area.(lat/long values)

- S right once to start editing.

- Using B to move field to field, and S to modify a field, edit the lat/long.

- When correct:  ENT to save.

Advanced G1000 MO Quick Reference Guide

Grid Search – Sarex “Slow Launch”

Modify all 4 Waypoints, create flight plan “grid box”

Do this after Engine Start, before or after takeoff.  Eyes outside while plane is taxiing – do this only while the airplane is stationary

KEY:

B		Turn big (outer) knob

S    		Turn small (inner) knob

RANGE	Press named knob or softkey

ENT	   	Press named hardkey

All Tasks start at Map Page 1 (hold CLR for 2 seconds)

Clear all existing Flight Plans

- FPL

- S to “Flight Plan Catalog” page.

- MENU

- S  to “Delete All”

- ENT

- ENT

Modify 4 existing Waypoints (eg GPTNE)

- B to WPT page group.

- S to “User Waypoint” page.

- Press S knob to get cursor.

- B down to “User Waypoint List”, continue to “GPTNE”.

    - ENT to get to detailed info & modify.

    - B to lat/long area.

    - S right one to start editing.

    - Using B to move field to field, and S to modify a field, edit the lat/long.

    - When correct:  ENT to save.

    - B right to next waypoint, eg GPTNW.

    - <Repeat for all 4>

- Hold CLR for 2 seconds ( Map Page 1

- RANGE out, PAN*, verify 4 GPT waypoints form a square.

Create a new Flight Plan

  - FPL

  - Press S knob to get cursor.

    - B to put cursor on blank line.

    - S right once to add a waypoint.

    - S left once to get to shortcuts

    - S right to “RECENT”

    - B right (down) to desired waypoint name

    - ENT

    - ENT

    - <Repeat for all waypoints>

Store a Flight Plan

- FPL

- S to “Active Flight Plan” page.

- MENU

- B to “Store Flight Plan”.

- ENT  (dialog asks to store to #1?)

- ENT   (yes, store it)

*PAN*

Press RANGE to get arrow pointer. Move “joy stick” to move pointer on map